## Slide 1
Networks R Us
Networking Technologies
October 2015
Presented by James Phillips

## Slide 2
Overview
Networking Technologies
Networking Tools
Emerging Network Technologies
Notes: Interconnected computers provide collaboration and sharing facilities that a stand-alone computer cannot.
In order to connect computers within an organisation a network is required.
In this presentation we will look at Networking Technologies, Networking Tools and Emerging Networking Technologies.

## Slide 3
Networking Technologies

## Slide 4
Networking Technologies
Network Operating Systems
Network Protocols
Network Layout
Network Devices
Notes: Any network will require a combination of a NOS (Network Operating System) and protocols to allow computers and other network devices to communicate with each other.
In this section of the presentation, we will look at NOS (Network Operating Systems), Protocols, Network Layout options and Devices.

## Slide 5
Network Operating Systems
An Operating System connects Hardware and Software
A Network Operating System provides services such as:
  Printer Sharing
  Email
  Security
Examples include:
Windows
Linux
Novell Netware (Open Enterprise Server)
OS X Server
Other Unix Variants
Notes: All computers (and also mobile devices such as iPads and smart phones) use an operating system to connect the hardware (physical device) to the software (applications).
A Network Operating System will provide services such as shared access to printers, disk space. Run services such as email, web-servers and database servers. A Network Operating System will also provide security management allowing control of access and access rights.
Available Network Operating Systems
Windows
Linux
Novell Netware (Open Enterprise Server)
OS X Server (for Apple Computers)
Other Unix Variants (including FreeBSD, Solaris, NetBSD)
.

## Slide 6
Network Operating Systems
Windows
  Common User Interface (with Desktop/Laptop PCs)
  Closed Source / Proprietary System with Licence Fees
  Supported with many applications available
Linux
  Free / Open Source System (no licence fees)
  Wide range of distributions (some with paid for support)
  Supported on multiple processor types
Others
  Low % of market share
  Some implementations tied to vendors hardware
Notes: Comparing the available Network Operating Systems:
Microsoft Windows is familiar as the most common Operating System on PC’s for desktop and laptops. The Server editions of Windows are used to control a client-server network where the clients are usually (but not exclusively) professional versions of the Windows Desktop Operating System which have client services built in. Windows is a proprietary, closed-source system for which users pay a licence fee to the Microsoft.
Linux is the common collective name for an Operating System built on the a freeware Linux Kernel (the core of the operating system). Based on Unix and with many free tools to support it, Linux is available in a wide range of distributions some with the facility of commercial (paid for) support. These distributions (such as Ubuntu) provide tools to make the operating system easier to install and administer.
Whilst Windows and Linux make up the majority of installed Network Operating Systems, Novell Netware (now branded as Open Enterprise Server) which was the dominant Network Operating System for PC’s in the late 1980’s and early 1990’s remains available.
Also, Apple Computer supplies a server edition of it’s Unix Based OS X Operating System which provides the same User Interface as the OS X used on Apple Computers. There are also many other Unix variants, usually supplied by hardware vendors such as IBM (AIX) or HP (HP-Unix) which are linked to the vendor’s equipment.

## Slide 7
Networking Protocols

## Slide 8
Protocols
Networking Protocols allow for communication between devices on a network.
Examples of protocols include:
SNMPv3
ICMP
FTP
TFTP
FTPS
HTTP/HTTPS
NTP
SMTP
Notes: To allow communication between devices on a network either for control or exchange of data, a set of rules or a protocol is used.
All of these protocols are in the Application Layer of the ISO OSI 7-Layer network model which is a conceptual model for communication systems that provides an abstraction from the actual structure or technology in use. The objective of this model is to allow interconnection and interoperability of different systems with standard protocols.

## Slide 9
Protocols
Notes: The ISO OSI 7-Layer network model is a conceptual model for communication systems that provides an abstraction from the actual structure or technology in use.
The purpose of this model is to allow interconnection and interoperability of different systems with standard protocols.
The protocols we are looking at are at the Application Layer.

## Slide 10
Protocols - SNMP
SNMP = Simple Network Management Protocol
SNMPv3 is the third version.
Used to control network devices such as routers.
Notes: SNMPv3 is the third version of the Simple Network Management Protocol that is used to control devices on the network such as routers.
This version of the protocol offers enhanced security over previous versions. SNMP is the protocol behind many network management tools allowing for remote configuration and status reporting.

## Slide 11
Protocols - ICMP
ICMP =Internet Control Message Protocol
Used by devices to report errors
Used by diagnostic tools ping and traceroute
Notes: ICMP or Internet Control Message Protocol, is a protocol in the Internet Protocol Suite commonly known as TCP/IP (Transmission Control Protocol/Internet Protocol) which provides end-to-end connectivity regardless of the networking technology in use.
ICMP is not concerned with data exchange, but is used by devices such as routers to report error messages. Some tools such as ping and traceroute are based on ICMP.

## Slide 12
Protocols - FTP
FTP = File Transfer Protocol
Used to transfer files between computers.
Variations include
TFTP = Trivial File Transfer Protocol
FTPS = File Transfer Protocol (Secure)
Notes: FTP is the File Transfer Protocol and is used to transfer files between computers. FTP is not a secure protocol, it was not designed to be. Weaknesses include sending all information in plain text (not encrypted) including usernames and passwords. This is common to many original protocols designed before TLS or SSL were introduced (after commercial use of the internet started).
TFTP is a simplified FTP variant that allows a client to get or put a file from/to a server. TFTP has no security. A common use of TFPT is in booting (starting) diskless or thin client workstations.
FTPS is the secure extension to FTP allowing for implicit and explicit methods of invoking the secure communication. Because of specifics of the way in which FTPS operates, there are situations where a firewall will block FTPS connections but allow unencrypted FTP connections.

## Slide 13
Protocols - HTTP
HTTP =HyperText Transfer
Used for distribution of documents and links.
Provides the core of the World Wide Web.
HTTPS is the secure (encrypted) version of the protocol.
Notes: HTTP or Hypertext Transfer Protocol is a protocol for distribution of documents and links. HTTP provides the core communication of information pages on the World Wide Web.
HTTPS is the secure (encrypted) version of the protocol.

## Slide 14
Protocols - NTP
NTP = Network Time Protocol
Allows for synchronization of computer clocks over networks
Counters latency (delays) in the transmissions.
Notes: NTP is the Network Time Protocol that allows for synchronization of computer clocks allowing for latency (delays) in the transmissions to avoid the clock being “slow” by the time the data took to be sent from the server back to the requesting machine.

## Slide 15
Protocols - SMTP
SMTP = Simple Mail Transfer Protocol
Standard method for email transmission.
Notes: SMTP is Simple Mail Transfer Protocol and is the standard method for email transmission.
SMTP is used for sending emails between mail servers, client software such as Microsoft Outlook may use different protocols to send and receive emails to the local mail server, but that server will use SMTP to relay the message onto any external mail servers.

## Slide 16
Network Layouts

## Slide 17
Network Layout
There are two key types of network:
  Wired/Cabled
  Wireless
Wireless networks are popular because:
  Flexible
  Require no fixed cabling/trunking
  Most new devices support Wireless Standards WiFi (802.11)
Wired/Cabled networks can be considered:
  Faster (better transmission speeds)
  More secure
Notes: In this section we look at the types of network and the configuration options available (the network topologies).
There are two key types of network, cabled and wireless. There are many types of cabling for a network. The type of cable to be used is dependent on the speed required and the length of the cable (determined by the distance between points on the network).
Wireless networks are popular because they are flexible and require no cables to be installed (or moved). Laptops, Tablets and Smart Phones now include WiFi connectivity (802.11) of some variant as standard which makes it simple to connect the device to a home or office network or to a hotspot at a hotel or on a train for example.
Wireless LAN (Local Area Networks) are linked via WiFi, although other technologies such as WiMAX exist for city-wide networking.

## Slide 18
Network Layout - Star
Notes: Star – each computer in the network is connected to a single switch, which provides connectivity between those computers and other network devices.

## Slide 19
Network Layout - Tree
Notes: Tree – used in larger organisations, this connects star networks together into a large network. One of the benefits of this is that the network is easier to administer.

## Slide 20
Network Layout - Ring
Notes: Ring – this topology has nodes which connect to exactly two other nodes. Data travels through each node along the way to its destination. The Ring topology is used in FDDI (Fiber Distributed Data Interface) where the network is connected using fiber optic cables which can extend the range of a network to as far as 120 miles (200km).

## Slide 21
Network Layout - Mesh
Notes: Mesh – A mesh network has multiple routes between devices connected to it (nodes) and routers are used to find the best route to a destination. A mesh network is resilient to damage. The BT telephone network is a mesh topology allowing for continuation of service even if cables are damaged by road works for example.

## Slide 22
Network Devices

## Slide 23
Network Devices
Devices are hardware items on the network.
Examples include:
  Servers
  Workstations
  Interconnection Devices
  Network Interface Cards
  Vendor Specific Hardware
Notes: Network devices are hardware that is part of the network.
In this section we will look at the various device types: Servers, Workstations, Interconnection Devices, Network Interface Cards and Vendor Specific Hardware.

## Slide 24
Servers
Servers control the network
Usually of a high specification
Typical servers on the network include:
Mail
Web
File
Groupware
Application
Proxy
Notes: Servers control the network. Some networks may have a single server; others may have several servers with dedicated tasks
Servers are usually more powerful than regular desktop PC’s. They come in a number of forms – Tower (like a desktop), Rack Mounted (where in the form of a pizza box the server will fit into a specially designed enclosure) or Blade (a number of bare motherboards fit into a single container).
On the next slides we look at the functions of these servers.

## Slide 25
Servers
Mail servers handle inbound/outbound emails
Web servers provide content to browsers
File servers provide storage and access controls
Notes: Mail servers move and store email, handling communication between users on the network and then to other organisations. This type of server uses the SMTP protocol.
Web servers provide content to browsers, typically using the HTTP/HTTPS protocol.
File servers provide storage for user files, often a file server will be used to centralise and share documents, with the advantage that there is a single set of files to backup (rather than trying to backup each users PC) and will allow for certain files or areas to be restricted to specific users or groups of users within the organisation.

## Slide 26
Servers
Groupware servers provide collaboration tools.
Application Servers provide access to software packages.
Proxy servers restrict internet access and provide connection sharing.
Notes: Groupware servers enable users to work together over the network or in some cases extend this over the internet to users outside of the organisation.
Application servers provide access to the software products a user of the network may need. Using an application server can reduce the costs associated with updating applications (the application is on a single server rather than on a number of client PCs).
Proxy servers are used to provide a filter between the users on the network and the wider internet. A proxy server can be used to block access to certain sites. A proxy may also be used to improve performance and provide connection sharing between users of a local network.

## Slide 27
Workstations
Computers for users are called workstations.
Two forms:
  Thick Client – has Operating System/Applications
  Thin Client – Minimal OS and no Applications
Notes: Computers for individual users to logon to are called workstations. A workstation needs only be powerful enough to handle it’s tasks. Some workstations will carry out processor intensive tasks whereas others will be lightly used.
A workstation that has locally installed software and a full client operating system is referred to as a Thick client. A workstation that has little or no locally installed software is referred to as a Thin client and accesses applications running on server on the network (or on a server accessed over the public internet).

## Slide 28
Network Interface Cards
Can be a plug in card or built-in
Has a unique identity (MAC address)
Provides a connector to a wired network
Or a radio interface for wireless networks
Notes: Computers in a network will have a Network Interface sometimes as a card that is plugged into the system other times the facilities will be built into the system.
Collectively the interface to the network (commonly an RJ45 connector for wired Ethernet) is described as a NIC or Network Interface Card.
A wireless solution will not require a cable as it uses a radio-based connection.
A NIC will have a MAC (Media Access Control) address which is a guaranteed unique identity for the specific device.

## Slide 29
Interconnection Devices
Connecting parts of a network together requires specific networking components.
These include:
  Hubs
  Repeaters
  Bridges
  Switches
  Routers
Notes: Hubs – on an Ethernet network a hub connects a number of devices to the network. The hub works at the physical layer of the OSI Model and simply passes inputs / outputs between connections.
Repeaters - (sometime hubs have repeater functionality) are used to boost signal allowing longer distances to be covered.
Bridges allow networks to be connected together, typically connecting multiple networks on the same physical site.
Switches – switches have largely replaced hubs in modern networks. A switch works at the data link layer of the OSI Model, allowing for the device to act intelligently passing data only to where it is required rather than on all ports. Communication is based on the MAC (Media Access Control) address of the network interface.
Routers are used to forward data between networks, working with multiple networks as opposed to a switch that works with a single network. The most common form of router is the home/small office router (sometimes combined with a hub) that allows users to connect through to websites etc on the internet.

## Slide 30
Vendor Specific Hardware
Vendor/Manufacturer Specific Items
Examples:
  HP Jet Direct – connects HP printer to network
  Proprietary Network Analysis Hardware
Notes: Vendor Specific Hardware
Some hardware connected to the network is specific to a vendor and works with items of that vendors technology in certain conditions. This may be a specific element of connectivity such as HP Jet Direct (a card which plugs into a HP Printer to allow it to be connected directly to the network) or that certain features are available only when components from the same vendor are used (an example could be a proprietary network performance analysis tool that works with only one vendors routers and switches).

## Slide 31
Networking Tools

## Slide 32
Networking Tools
Networking Tools assist in the management of a network.
We will look at three types of tool:
Fault Management
Performance Management
Detection of Network Assets
Notes: Networking Tools exist to assist in the management of the network. In this section we will look at three categories:
Fault Management
Performance Management
Detection of Network Assets

## Slide 33
Fault Management
Fault Management:
  Detecting Problems
  Providing Alerts
  Potential to provide automated fixes
Notes: Fault Management refers to detecting where problems are and fixing them. When a fault or event occurs, a network component will often send a notification to the network operator using a protocol such as SNMP (Simple Network Management Protocol).
Typically a management console allows a network operator / manager to see any faults that are being reported.
Some fault management systems allow for events to trigger automated solutions (launching a program or script to take corrective action) or performs an alerting task such as sending an email/SMS to a human operator.

## Slide 34
Performance Management
Performance Management:
View network performance such as:
  Bandwidth/Throughput
  Latency
  Uptime
Notes: Performance Management is understanding how well the network is operating and assisting in configuring it to work better.
Typical metrics are Bandwidth/Throughput (measure of the amount of data that can be transferred in a defined time period); Latency (the amount of time it takes for data to travel across the network); Uptime (the time period for which a network/connection is functioning and usable).
For performance measurement, operators typically measure the performance of their networks at different levels. They either use per-port metrics (how much traffic on port 80 flowed between a client and a server and how long did it take) or they rely on end-user metrics such as how fast did the login page load for a specific user. Per-port metrics are collected using flow-based monitoring and protocols, whereas end-user metrics are collected through web logs, synthetic monitoring, or real user monitoring.
Performance Management tools typically provide both a real-time view of the network performance and historic reporting. This helps to identify periods where the service being provided was not as expected or breaches an agreed level.

## Slide 35
Detection of Network Assets
Detection of Network Assets:
Automated discovery of items on the network
Can include finding types/models of equipment
Can include “agents” which inspect PC’s for installed software.
Notes: Detection of Network Assets is the use of a software program to determine the various networking hardware devices that are on the network and in some cases gain information of the performance of these assets. Some tools will go as far as being able to report on the configuration and installed software of computers on the network.
A tool to discover network assets may be used to map/discover a large network and identify what is connected to it. This may be due to merging of networks or to determine any unauthorised additional devices. Tools which can do a discovery of assets installed on a PC may be used to assist with licence compliance.

## Slide 36
Networking Tools
Example Networking Tools:
Opsview
CiscoWorks
Wireshark
Microsoft System Center Operations Manager
Notes: Examples of networking tools include
Opsview – a tool for getting a total view of a network including assets
and performance.
CiscoWorks – a tool for configuring and managing Cisco networking
equipment.
Wireshark – a network protocol analysis tool.
Microsoft SCOM (System Center Operations Manager) – a tool for
managing Operating Systems over a network.
We will look at a summary of each.

## Slide 37
Opsview
Opsview's network monitor software allows you to correlate data from a wide variety of network devices and applications to give you a total view of your physical, virtual and cloud network infrastructures in a single place.
There are three versions of the tool: Opsview Atom open source network monitoring (free) or if you need to monitor complex business environments choose Opsview Pro (for SMEs) or Opsview Enterprise (for deployments monitoring up to 20,000 devices).
Notes: Opsview
Opsview's network monitor software allows you to correlate data from a wide variety of network devices and applications to give you a total view of your physical, virtual and cloud network infrastructures in a
There are three versions of the tool: Opsview Atom open source network monitoring (free) or if you need to monitor complex business environments choose Opsview Pro (for SMEs) or Opsview Enterprise (for deployments monitoring up to 20,000 devices).

## Slide 38
CiscoWorks
CiscoWorks is a suite of powerful management tools that simplify the configuration, administration, monitoring, and troubleshooting of Cisco networks.
CiscoWorks can be used for:
Improving the accuracy and efficiency of the network operations staff
Increasing the overall availability of the network by simplifying configuration and quickly identifying and fixing network problems
Maximizing network security through integration with access control services and audit of network-level changes
Notes: CiscoWorks is a suite of powerful management tools that simplify the configuration, administration, monitoring, and troubleshooting of Cisco networks.
CiscoWorks can be used for:
Improving the accuracy and efficiency of the network operations staff
Increasing the overall availability of the network by simplifying configuration and quickly identifying and fixing network problems
Maximizing network security through integration with access control services and audit of network-level changes

## Slide 39
Wireshark
Wireshark is a network protocol analyser, it is used for network troubleshooting, analysis, software and communications protocol development, and education. The tool runs on Windows, Linux, OS X, and Unix operating systems such as Solaris, FreeBSD and NetBSD.
Live data can be read from various physical implementations including Ethernet, 802.11, USB and FDDI. The data captured can be viewed in different ways and output to various formats such as XML, CSV or plain text.
Notes: Wireshark is a network protocol analyser, it is used for network troubleshooting, analysis, software and communications protocol development, and education. The tool runs on Windows, Linux, OS X, and Unix operating systems such as Solaris, FreeBSD and NetBSD.
Live data can be read from various physical implementations including Ethernet, 802.11, USB and FDDI. The data captured can be viewed in different ways and output to various formats such as XML, CSV or plain text.

## Slide 40
Microsoft SCOM
Microsoft System Center Operations Manager (SCOM) is a management system for operating systems and hypervisors which works across different platforms. The tool uses a single interface that shows state, health and performance information of computer systems.
The tool also provides alerts generated according to some availability, performance, configuration or security situation being identified. It works with Microsoft Windows Server and Unix-based hosts.
Notes: Microsoft System Center Operations Manager
Microsoft System Center Operations Manager (SCOM) is a management system for operating systems and hypervisors which works across different platforms. The tool uses a single interface that shows state, health and performance information of computer systems. The tool also provides alerts generated according to some availability, performance, configuration or security situation being identified. It works with Microsoft Windows Server and Unix-based hosts.

## Slide 41
Emerging Technologies

## Slide 42
Emerging Technologies
Emerging Networking Technologies:
Software Defined Networks
Edge Computing
Open Source Hardware
Notes: In this section we will look at three emerging technologies in the Networking area:
Software Defined Networks – a change in the way in which networks are architected. A software defined network (SDN) decouples control and forwarding functions, allowing network control to be directly programmable. This allows for software to recognise and optimize network traffic flows where previously manual involvement would have been required.
Edge Computing – pushes applications, data and services from the centralised areas of the network to the logical extremities (the edge). Typical applications are where devices may not be continuously attached to the network such as tablets and smartphones, but also sensors and other devices commonly described as the Internet of Things (IoT).
Open Source Hardware – Open Source Software (such as Linux) has powered much of the growth of the internet. Initiatives in Open Source Hardware (OSH) are resulting in freely available designs for powerful, environmentally friendlier devices which are not subject to any form of vendor lock-in.

## Slide 43
Software Defined Networks
Software Defined Networking allows for networks to be controlled by software so that they can be automatically and dynamically reconfigured.
This emerging technology changes the way that the network is thought of. It is a core component (along with Virtual Machines) of IaaS – Infrastructure as a Service.
Notes: SDN architectures separate network control and forwarding functions, enabling network control to become directly programmable and the underlying infrastructure to be abstracted from applications and network services.

## Slide 44
Software Defined Networks
Software Defined Networking (SDN) is an architecture designed to be:
  Dynamic
  Manageable
  Cost-effective
  Adaptable
OpenFlow a new protocol allows for controllers (software) to determine the path of network packets through the network of switches.
Notes: Software Defined Networking (SDN) is an architecture designed to be dynamic, manageable, cost-effective, and adaptable. It is understood to be more suitable for the high-bandwidth, dynamic nature of today's applications than traditional networking configurations. SDN architectures decouple network control and forwarding functions, enabling network control to become directly programmable and the underlying infrastructure to be abstracted from applications and network services.
The OpenFlow protocol is a foundational element for building SDN solutions.

## Slide 45
Software Defined Networks
The SDN Architecture is:
  Directly Programmable
  Agile
  Centrally Managed
  Programmatically Configured
  Open Standards-Based and Vendor-Neutral.
Notes: The SDN architecture is:
Directly programmable: Network control is directly programmable because it is decoupled from forwarding functions.
Agile: Abstracting control from forwarding lets administrators dynamically adjust network-wide traffic flow to meet changing needs.
Centrally managed: Network intelligence is (logically) centralized in software-based SDN controllers that maintain a global view of the network, which appears to applications and policy engines as a single, logical switch.
Programmatically configured: SDN lets network managers configure, manage, secure, and optimize network resources very quickly via dynamic, automated SDN programs, which they can write themselves because the programs do not depend on proprietary software.
Open standards-based and vendor-neutral: When implemented through open standards, SDN simplifies network design and operation because instructions are provided by SDN controllers instead of multiple, vendor-specific devices and protocols.

## Slide 46
Edge Computing
As the name implies, edge computing pushes computing power to the edges of a network, so instead of devices like drones or smart traffic lights needing to call home for instructions or data analysis, they can perform analytics themselves on streaming data and communicate with other devices to accomplish tasks.
Edge computing requires that information is accessible so devices may store some of the data locally and automatically synchronise when they are connected to the relevant network.
Notes: As the name implies, edge computing pushes computing power to the edges of a network, so instead of devices like drones or smart traffic lights needing to call home for instructions or data analysis, they can perform analytics themselves on streaming data and communicate with other devices to accomplish tasks.
Edge computing requires that information is accessible so devices may store some of the data locally and automatically synchronise when they are connected to the relevant network.

## Slide 47
Open Source Hardware
Like Open Source Software (OSS), Open Source Hardware promotes free to use designs for various networking technology. The Open Compute Project (spawned from work by Facebook on building efficient servers) is looking to promote open designs that where:
All infrastructure technology and energy consumption (renewable and non-renewable) has environmental impact; we will minimize environmental impact whenever possible
Notes: Whilst not directly a technology in the sense of WiFi or Gigabit broadband, Open Source Hardware is a technology that has real potential as it emerges; if OSH has the same effect as OSS the costs (in monetary and environmental terms) of powerful networks may be reduced.

## Slide 48
Impact of Emerging Technology

## Slide 49
Software Defined Networks
Software Defined Networking (SDN) has a number of potential impacts:
  IaaS/Scaling
  Increased Utilisation
  Reduced User Administration
Notes: IaaS/Scaling– combined with Virtual Machines/Containers a SDN can allow for a whole network including servers to be defined securely in a cloud environment and reconfigured dynamically. This IaaS can then be automatically scaled to cater for application load activating more servers and changing routing at peak times without human intervention.
Increased Utilisation – by defining networks dynamically (especially when combined with VM’s) more utilisation can be achieved from a given number of physical hardware servers. In turn this has a reduced equipment requirement which requires less manufactured hardware and importantly less power for both the hardware and associated data centre cooling. A direct environmental benefit.
Reduced User Administration – it is expected that identity and policy management challenges can be addressed by using global definitions and allowing the SDN to deliver access controls to the point-of-need (where the user is connecting to the network) which in an increasingly mobile workforce could save much administration time.

## Slide 50
Edge Computing
Researching the potential impact of Edge Computing – the following (taken from an article on govtech.com) provides the clearest description of the impact.
Edge computing would solve many of the most difficult problems facing robotics and computing infrastructure. A swarm of air- and land-based drones examining a remote forest fire, a collapsed building or a vast tract of farmland is today challenged by an inability to connect and transmit large quantities of data over wireless networks or to receive instructions from a central controller in a timely fashion. These problems are exacerbated by the confusing terrain of disaster environments, but edge computing circumvents these obstacles.
The impact therefore, could be far more autonomous activity by network connected (or sometimes connected) devices such as drones for research. Allowing for reduced risk for humans in such a situation.
Notes: Edge computing will allow systems to degrade gracefully, work autonomously and deliver information to decision-makers faster and more efficiently.
Edge computing would solve many of the most difficult problems facing robotics and computing infrastructure. A swarm of air- and land-based drones examining a remote forest fire, a collapsed building or a vast tract of farmland is today challenged by an inability to connect and transmit large quantities of data over wireless networks or to receive instructions from a central controller in a timely fashion. These problems are exacerbated by the confusing terrain of disaster environments, but edge computing circumvents these obstacles.

## Slide 51
Open Source Hardware
The potential impact of Open Source Hardware is a reduced environmental impact – both in the manufacture and operation of data center equipment (Servers and associated networking equipment).
According to the Open Compute Project:
The Open Compute server's vanity-free design eliminates nearly 6 pounds of material per server, reducing the amount of materials that need to be produced, transported, assembled, and eventually, disassembled. "Designing out," or excluding, all non-essential features and non-relevant elements from the Open Compute servers allows for a custom chassis that minimizes the overall part count, accelerates assembly, and removes elements like a front panel, paint, and logos. Additionally, Open Compute servers can operate in a higher-temperature environment, reducing the overall cooling load required in a data center.
Notes: As we are in a period of increased data center usage with cloud computing and web-based applications being commonplace, with storage and computing being centralised in part. Any efforts to reduce the environmental impact of data centres is welcomed. Whist the OCP has worked so far to bring open plans for servers and racks. The mission to do the same for other networking components is encouraging:
We’re bringing to networking the guiding principles that OCP has brought to servers & storage, so that we can give end users the ability to forgo traditional closed and proprietary network switches - in favor of a fully open network technology stack. Our initial goal is to develop a top-of-rack (leaf) switch, while future plans target spine switches and other hardware and software solutions in the space.

## Slide 52
Summary
Network Technologies
Network Operating Systems
Network Protocols
Network Layouts
Network Devices
Networking Tools
Fault Management
Performance Management
Asset Detection
Emerging Networking Technologies
Impact of Emerging Technologies
Notes: In this presentation we have looked at the technologies which make up a network (Operating Systems, Protocols, Layouts/Topologies and Devices).
We have looked at Networking Tools and their purpose (Fault Management, Performance Management and Asset Detection).
We have looked at three emerging technologies in the networking arena – Software Defined Networks, Edge Computing and Open Source Hardware; and looked at the impact of these technologies.

## Slide 53
Bibliography/Sources
http://www.opsview.com/network-monitoring-software
http://www.cisco.com/c/en/us/products/cloud-systems-management/ciscoworks-lan-management-solution-3-2-earlier/index.html
https://en.wikipedia.org/wiki/Wireshark
https://en.wikipedia.org/wiki/System_Center_Operations_Manager
http://www.techsoupforlibraries.org/cookbook-3/networking-and-security/tools/network-performance-metrics-defined
https://en.wikipedia.org/wiki/Fiber_Distributed_Data_Interface
https://en.wikipedia.org/wiki/OSI_model
https://en.wikipedia.org/wiki/Internet_protocol_suite
https://en.wikipedia.org/wiki/Simple_Mail_Transfer_Protocol
https://en.wikipedia.org/wiki/Comparison_of_operating_systems
https://en.wikipedia.org/wiki/Software-defined_networking
http://www.informationweek.com/cloud/10-emerging-it-trends-from-gartner-symposium/d/d-id/1322569?_mc=RSS_IWK_EDT&image_number=4
http://www.informationweek.com/cloud/10-emerging-it-trends-from-gartner-symposium/d/d-id/1322569?_mc=RSS_IWK_EDT&image_number=7
http://www.govtech.com/transportation/Is-Edge-Computing-Key-to-the-Internet-of-Things.html
http://www.opencompute.org/about/energy-efficiency/
http://www.opencompute.org/projects/networking/
http://www.opencompute.org/about/mission-and-principles/
BTEC Level 3 Information Technology Book 1 - Anderson, Jarvis, Kaye, Lawson, McGill, Phillips, Smith
Computer Architecture and Communications - Neil Willis