## Slide 1: WEP
WEP stands for Wired Equivalent Privacy.
This doesn't mean it can be used on a wired network, but it provides the same privacy as a wired network.
Can use two types of authentication:
  Open system
  Shared Key
B

## Slide 2: WEP : Open Systems
In Open System authentication, the WLAN client doesn't need to provide its credentials to the Access Point during authentication.
Any client can authenticate with the Access Point and then attempt to associate.
In effect, no authentication occurs. Subsequently WEP keys can be used for encrypting data frames.
At this point, the client must have the correct keys.
B

## Slide 3: WEP : Shared Key
In Shared Key authentication, the WEP key is used for authentication in a four-step challenge-response handshake:
  The client sends an authentication request to the Access Point.
  The Access Point replies with a clear text challenge.
  The client encrypts the challenge-text using the configured WEP key and sends it back in another authentication request.
  The Access Point decrypts the response. If this matches the challenge text, the Access Point sends back a positive reply.
After the authentication and association, the pre-shared WEP key is also used for encrypting the data frames using RC4.
B

## Slide 4: Other types of WEP
WPA
WEP2
WEP+
Dynamic WEP
B